## Slide 1
WEEK 02 / COORDINATE FRAMES
Coordinate frames & tf2
Describe the same point. Move between frames.
Robotics & Autonomous Systems · ROS 2 Jazzy
01
Understand frames
Read the math
Inspect the demo
pA = RAB pB + tAB
20 min concepts · 25 min code, demo & questions
Notes: Timing: 0 minutes.
Week 2: understand why coordinates need a frame, how rotation and translation are represented, and how tf2 maintains relationships over time. Audience knows Python and has little geometry/networking background. Title is untimed. Teaching slides total 20 minutes; demo is 25 minutes: 5 code, 10 static/RViz, 5 moving/time, 5 checkpoint. The revised presentation contains exactly 18 visible slides. Use the reference sheet for deeper study instead of trying to derive all conversions live. All seven existing Week 2 files were read. Professor sources reviewed: 2-Frames.pdf and the neighboring-transform/FK material in 3-Kinematics.pdf. Demo code, README, RViz and teaching notes remain unchanged.
Sources:
https://docs.ros.org/en/jazzy/Concepts/Intermediate/About-Tf2.html

## Slide 2
WEEK 02 / COORDINATE FRAMES
Why do coordinates need a frame?
One physical target. Several coordinate descriptions.
Robotics & Autonomous Systems · ROS 2 Jazzy
02
x
z
y
world
x
z
y
robot
x
z
y
camera
same target
A camera measurement needs a robot-frame destination.
Notes: Timing: 1 minutes.
Visual: three labelled coordinate axes looking at one target. A frame is an origin plus axes; the target is unchanged, but its coordinates depend on that origin and basis. A camera can report a point without telling the arm where it is in robot coordinates. Ask what happens if the robot treats camera coordinates as base coordinates. Frame conversions connect sensor drivers, perception, localization and camera-guided motion. PointStamped carries both frame_id and observation time; an unlabelled three-number tuple is ambiguous. The illustration is conceptual, not a calibration of the demo camera. Do not confuse movement of a physical object with a change in its coordinate description.
Sources:
https://docs.ros.org/en/jazzy/Concepts/Intermediate/About-Tf2.html

## Slide 3
WEEK 02 / COORDINATE FRAMES
What are TF and tf2?
A geometric relationship, managed by a ROS 2 library.
Robotics & Autonomous Systems · ROS 2 Jazzy
03
Transform (TF) · mathematics
Relationship between frames Rotation + translation Converts point coordinates
Ap = ARB Bp + AtB
tf2 · ROS 2 library
Manages frame relationships Static + time-dependent data Looks up and applies transforms Follows multi-frame chains
Frame = origin + coordinate axes.
A transform is the mathematics; tf2 manages and applies it in ROS 2.
Notes: Timing: 1 minutes.
A rigid transform is a geometric mapping. TF is also used informally for the ROS frame system; distinguish the mathematical operation from the tf2 library. tf2 buffers static/time-dependent relationships and composes or inverts connected paths. Another component supplies calibration or estimated poses. Leading superscripts follow professor Lecture 2, printed slides 7 and 13–14.

## Slide 4
WEEK 02 / COORDINATE FRAMES
Always check the conventions
ROS defines the standard. Always check the conventions you use.
Robotics & Autonomous Systems · ROS 2 Jazzy
04
ROS body
x forward · y left z up
ROS optical
x right · y down z forward
Translation: meters (m) Rotation angles: radians (rad)
Right-handed: x × y = z
Check: handedness · transform direction · Euler axes/order · row/column vectors
Check the conventions of every data source, library, and API.
Notes: Timing: 1.5 minutes.
ROS standards use right-handed frames, meters and radians. Body axes are x forward, y left, z up; optical axes are x right, y down, z forward. Always verify the actual data and library: transform direction, Euler axes/sequence, handedness, units and column/row vectors. A generic right-hand picture demonstrates chirality, not a prescribed attachment of each axis to one finger. Keep the labels in the supplied picture unchanged. ROS quaternion ordering is discussed later on slide 13. The existing teaching camera frame is simplified, not an optical frame. Sources: REP 103 and professor Lecture 2 printed slides 7, 15 and 50.

## Slide 5
WEEK 02 / COORDINATE FRAMES
Read the direction correctly
The point stays still; its coordinate tuple changes.
Robotics & Autonomous Systems · ROS 2 Jazzy
05
Ap = ARB Bp + AtB
B coordinates
A coordinates
ATB
Pose of B in A · maps B → A
A
B
p
AtB
Origin of frame B, expressed in frame A.
Notes: Timing: 1.5 minutes.
Read ^A T_B as the pose of B expressed in A, mapping B coordinates into A coordinates. The leading superscript names the expression/destination frame. The translation ^A t_B is the origin of B expressed in A. Keep the physical point fixed in the two-frame diagram: only its coordinate representation changes. The equation and B-to-A flow restore the original math-reading approach. Professor Lecture 2 printed slides 13 and 19–22.

## Slide 6
WEEK 02 / COORDINATE FRAMES
Elementary rotations & Euler angles
Fixed-axis XYZ: roll about x, pitch about y, yaw about z.
Robotics & Autonomous Systems · ROS 2 Jazzy
06
Rx(φ) · roll
Ry(θ) · pitch
Rz(ψ) · yaw
1
0
0
0
cφ
−sφ
0
sφ
cφ
cθ
0
sθ
0
1
0
−sθ
0
cθ
cψ
−sψ
0
sψ
cψ
0
0
0
1
R = Rz(ψ) Ry(θ) Rx(φ)
90° x then z: ex → ey · z then x: ex → ez
Pitch = ±90°: roll and yaw couple (gimbal lock). Euler singularity; physical rotation remains possible.
▶ Gimbal Lock — Video Demonstration (start at 2:20)
Notes: Timing: 2 minutes.
c and s denote full-angle cosine and sine for the indicated angle. Matrices use right-handed positive rotations on column vectors. Fixed/extrinsic XYZ RPY means rotate about the original x, then y, then z axes; the product acts rightmost first. Rz(+90 degrees)e_x=e_y. Reversing the x/z rotation order changes the result. At pitch +90 degrees only yaw-roll is identifiable; at -90 degrees only yaw+roll is identifiable. This is an Euler-coordinate singularity, not a physical inability to rotate. The optional video opens at 140 seconds (2:20); keep video viewing brief within the session timing. Professor Lecture 2 printed slides 15–16, 26 and 29.

## Slide 7
WEEK 02 / COORDINATE FRAMES
Rotation matrices describe frame axes
Each column is an axis of frame B expressed in frame A.
Robotics & Autonomous Systems · ROS 2 Jazzy
07
Three columns · three unit axes
ARB = [ Ax̂B AŷB AẑB ]
B axes, written using A coordinates.
RTR = I det(R) = +1
xA
yA
xB
yB
⊙ zA = zB (out)
A: blue · B: teal
Notes: Timing: 1.5 minutes.
Each column of ^A R_B is one unit axis of B expressed in A. The picture uses coincident origins and common +z pointing out of the page, with B rotated relative to A. Read a column by asking where a unit step along that B axis points in A. Orthogonal unit columns give R^T R=I; determinant +1 selects a right-handed proper rotation. Professor Lecture 2 printed slides 12–13.

## Slide 8
WEEK 02 / COORDINATE FRAMES
Homogeneous transformations
Same 4 × 4 transformation, two notations.
Robotics & Autonomous Systems · ROS 2 Jazzy
08
Block form · 2 × 2 blocks
Expanded form · 4 × 4 entries
ATB =
ARB
AtB
0T
1
=
r11
r12
r13
tx
r21
r22
r23
ty
r31
r32
r33
tz
0
0
0
1
R: 3 × 3 · t: 3 × 1 · 0T: 1 × 3
Bottom row: 0 0 0 1
Ap = ARB Bp + AtB
Point [p; 1] includes translation. Direction [d; 0] does not.
Notes: Timing: 1.5 minutes.
These are two notations for the same 4x4 matrix, not a 2x2 numerical transform versus a 4x4 transform. The left side partitions the matrix into a 3x3 rotation, 3x1 translation, 1x3 zero row, and scalar 1. The right side expands those blocks into all 16 entries. The vector t is the B origin expressed in A. For a homogeneous point [p;1], multiplication includes translation. A direction [d;0] ignores translation. Professor Lecture 2 printed slides 19–22.

## Slide 9
WEEK 02 / COORDINATE FRAMES
Compose and invert
Apply right to left. Matrix multiplication order matters.
Robotics & Autonomous Systems · ROS 2 Jazzy
09
A
B
C
ATC = ATB BTC
Match the inner frame indices: B → B.
T-1 =
RT
−RTt
0
1
Subtract the translation, then rotate back.
Notes: Timing: 1 minutes.
Match B in ^A T_B ^B T_C: C coordinates first map to B, then A. Frame-index cancellation is a mnemonic, not cancellation of matrices. Order matters. Inverse translation is -R^T t, not merely -t. Subtract t from the input point, then rotate back. Tree arrows on later slides name parent-child relationships rather than coordinate flow. Professor Lecture 2 printed slides 16 and 22.

## Slide 10
WEEK 02 / COORDINATE FRAMES
Why use quaternions?
Three practical reasons for a different rotation representation.
Robotics & Autonomous Systems · ROS 2 Jazzy
10
01
Avoid Euler gimbal lock
Represent every orientation without Euler-angle singularities.
02
Compose 3D rotations
Combine rotations using ordered quaternion multiplication.
03
Interpolate smoothly
SLERP gives smooth changes between orientations.
Notes: Timing: 1 minutes.
Introduce motivation before formulas: quaternions do not have Euler-angle gimbal-lock singularities, compose rotations conveniently, and support smooth orientation interpolation with SLERP. They still need an agreed convention, normalization, and separate translation. They are not unique: sign equivalence is introduced on the next slide. Professor Lecture 2 printed slide 40.

## Slide 11
WEEK 02 / COORDINATE FRAMES
Quaternion representation
A quaternion has one scalar component and three vector components.
Robotics & Autonomous Systems · ROS 2 Jazzy
11
q = (w, v) = (w, x, y, z)
w: scalar part
v = (x, y, z): vector part
w = cos(α/2)
v = K sin(α/2)
K = (kx, ky, kz), ‖K‖ = 1 · α: rotation angle
w² + x² + y² + z² = 1
q and −q: same 3D rotation
Notes: Timing: 1.5 minutes.
q=(w,v)=(w,x,y,z) uses mathematical scalar-first Hamilton notation. The bold v is a three-vector, not a fifth component. With unit rotation axis K=(kx,ky,kz) and right-hand angle alpha: w=cos(alpha/2), v=K sin(alpha/2). Thus x=kx sin(alpha/2), y=ky sin(alpha/2), z=kz sin(alpha/2). Four numbers constrained to unit norm give three orientation degrees of freedom. q and -q encode the same rotation, not inverse rotations. Professor Lecture 2 printed slides 34 and 40.

## Slide 12
WEEK 02 / COORDINATE FRAMES
Quaternion multiplication & points
The Hamilton product ⊗ composes rotations. Its order matters.
Robotics & Autonomous Systems · ROS 2 Jazzy
12
q1 ⊗ q2 = (w1w2 − v1·v2,
w1v2 + w2v1 + v1×v2)
(0, Aprot) = qAB ⊗ (0, Bp) ⊗ qAB-1
Ap = Aprot + AtB
Unit q: inverse = conjugate · rotate first, then add translation.
Notes: Timing: 1.5 minutes.
For q1=(w1,v1) and q2=(w2,v2), the first component of the Hamilton product is scalar w1w2-v1 dot v2. The second is vector w1v2+w2v1+v1 cross v2. Read the formula as scalar/vector parts, not component-wise multiplication. Composition is ordered: q_AC=q_AB tensor q_BC. Use a pure quaternion (0,p) in the sandwich q tensor (0,p) tensor q inverse; read the vector part as the rotated point. The q_AB orientation maps B coordinates to A coordinates. Add the separately expressed translation ^A t_B afterward. Unit inverse is the conjugate (w,-v). Sign flip is not generally the inverse. Professor Lecture 2 printed slides 35–38.

## Slide 13
WEEK 02 / COORDINATE FRAMES
How tf2 uses quaternions
The library handles the rotation algebra for you.
Robotics & Autonomous Systems · ROS 2 Jazzy
13
tf2 uses quaternions behind the scenes for rotations. Translation remains a separate 3D vector.
ROS component order
(x, y, z, w)
Identity rotation
(0, 0, 0, 1)
Unit norm is required. tf2 handles composition and inversion when you look up transforms between frames.
Notes: Timing: 1 minutes.
tf2 represents buffered rotation samples with quaternions alongside separate translation vectors. You normally ask for a transform between frames; the library follows the chain and handles composition and inversion. Some internal geometry operations also use rotation matrices, so do not imply every operation is performed exclusively in quaternion algebra. ROS ordering is x,y,z,w, while the previous mathematical slide used scalar-first w,x,y,z. A rotation quaternion must have unit norm; normalize valid nonzero numerical values before use. Identity is (0,0,0,1); all-zero is invalid. This slide focuses on the role of quaternions inside tf2. Sources: ROS 2 Jazzy tf2 Quaternion and TransformStorage implementations; Quaternion Fundamentals.

## Slide 14
WEEK 02 / COORDINATE FRAMES
The frame tree
Parent → child edges describe the frame relationships.
Robotics & Autonomous Systems · ROS 2 Jazzy
14
world
base_link
camera_mount
camera_frame
dynamic · moving_base
static · static_frames
One parent per child · one authority per edge · no cycles
Disconnected trees have no transform path.
Robot joints create dynamic transforms between neighboring links. Chain them to obtain the end-effector pose: forward kinematics.
Notes: Timing: 1 minutes.
world -> base_link is dynamic (solid blue); the camera edges are static (dashed teal). Arrows name parent-child relationships; a stored child pose in its parent maps child coordinates to parent coordinates. One parent per child, one authoritative broadcaster per edge, no cycles. Disconnected trees have no connecting transform path. A frame is not a ROS node. Movable robot joints determine transforms between neighboring links; chaining them gives forward kinematics. This is a conceptual connection, not a change to the existing teaching frames. Professor Lecture 3 printed slides 12–13.

## Slide 15
WEEK 02 / COORDINATE FRAMES
How tf2 works
Publish edges. Buffer samples. Look up a connected path.
Robotics & Autonomous Systems · ROS 2 Jazzy
15
static_frames
/tf_static
moving_base
/tf
Listener + Buffer
Lookup
Several publishers · each listener has its own buffer
Notes: Timing: 1 minutes.
Timing: 1 minutes.
Visual: static_frames and moving_base feed /tf_static and /tf, then listener/buffer and lookup. StaticTransformBroadcaster uses durable static data suitable for late listeners; TransformBroadcaster streams dynamic samples. TransformStamped includes header.frame_id parent, child_frame_id child, timestamp, translation and quaternion. Several nodes can publish different edges. Each TransformListener populates its own Buffer; there is no central lookup server. DDS transports samples between endpoints; executor callbacks consume them and fill the buffer. Lookup then performs geometry and time selection locally. These responsibilities are distinct. In the scripts, point_transformer creates Buffer and TransformListener, receives data while spinning, and calls lookup in its timer. Static data is time-independent, but publisher lifetime matters for late discovery; leave the existing static script spinning.
Sources:
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Static-Broadcaster-Py.html
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Listener-Py.html

## Slide 16
WEEK 02 / COORDINATE FRAMES
Transform at the measurement time
A moving robot makes an old observation different from a new one.
Robotics & Autonomous Systems · ROS 2 Jazzy
16
Observation at tₘ
Now
Use the transform at tₘ.
Latest is not acquisition time.
Finite history · consistent clocks · preserve the stamp
Notes: Timing: 1 minutes.
Timing: 1 minutes.
Visual: acquisition time and current time on a timeline. Time() requests latest common usable transform, not necessarily now. Real observations need the transform at their acquisition timestamp when the chain is dynamic. The demo camera-to-base relationship is static, so latest lookup there is valid. moving_base adds time dependence only between world and base_link. transform_point.py restores the input stamp after do_transform_point, so RViz can convert both point messages into world at the same measurement time. The synthetic point stays fixed in camera coordinates and moves with the robot; a real world-fixed target would change its camera coordinates. History is finite; requests too old or newer than buffered dynamic samples raise extrapolation. Missing frames and disconnected paths fail too. Match clock sources and use_sim_time; bounded waiting/retry can allow data to arrive, while blocking the only executor thread may prevent listener callbacks. Existing code does not simulate delayed camera observations.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/src/cache.cpp
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Listener-Py.html

## Slide 17
WEEK 02 / COORDINATE FRAMES
Inspect and predict
Predict the display before changing its reference frame.
Robotics & Autonomous Systems · ROS 2 Jazzy
17
ros2 run tf2_ros tf2_echo base_link camera_frame
ros2 run tf2_ros tf2_echo world base_link
lookup_transform(target, source, time)
Predict: what happens when we change the RViz Fixed Frame from base_link to world?
Notes: Timing: 1 minutes.
tf2_echo base_link camera_frame shows camera pose in base. lookup_transform(target,source,time) converts source coordinates into target coordinates. Ask for a prediction before switching the display reference. Expected insight: the display reference and apparent coordinates/motion can change, while the physical relationships remain unchanged. Coordinate descriptions of the same physical point still coincide when expressed in a common frame. The world frame must be connected. Preserve all existing commands and demo behavior.

## Slide 18
WEEK 02 / COORDINATE FRAMES
Live demo: read, run, predict
Three steps · predict first, then connect the output to the mathematics.
Robotics & Autonomous Systems · ROS 2 Jazzy
18
world
base_link
camera_mount
camera_frame
dynamic · moving_base
static · static_frames
1 Inspect the transform · camera coordinates → base coordinates
ros2 run tf2_ros tf2_echo base_link camera_frame
2 Transform the point · compare with the mathematics
Cp = (0.2, 0, 1) → Bp = (0, 0.2, 1.5)
3 Explain a failure · missing frame or disconnected tree?
Notes: Timing: 25 minutes.
Timing: 25 minutes for the existing demonstration and questions. 1 INSPECT: tf2_echo base_link camera_frame reports camera pose in base: Rz(+90 degrees), translation (0,0,0.5) m. 2 TRANSFORM: use the existing lookup and point transformation to connect the original camera point (0.2,0,1) to the base point (0,0.2,1.5). Rotate about +z by 90 degrees, then add 0.5 m along base z. Connect this to the homogeneous-transform and quaternion formulas. There is no separate numerical-example slide. 3 FAILURE: explain a missing-frame startup/recovery or disconnected-tree case; a buffer cannot infer a missing relationship. Unavailable timestamps on dynamic edges are a conceptual additional failure because transform history is finite. Static camera/base edges do not demonstrate dynamic extrapolation. RViz is optional: compare fixed frames base_link and world when the world transform is connected; the same physical points remain coincident. Presentation production does not run, modify, or rehearse the demo.