## Slide 1
WEEK 02 / COORDINATE FRAMES
Coordinate frames & tf2
Describe the same point. Move between frames.
Robotics & Autonomous Systems · ROS 2 Jazzy
01
Understand frames
Read the math
Inspect the demo
pA = RAB pB + tAB
20 min concepts · 25 min code, demo & questions
Notes: Timing: 0 minutes.
Week 2: understand why coordinates need a frame, how rotation and translation are represented, and how tf2 maintains relationships over time. Audience knows Python and has little geometry/networking background. Title is untimed. Teaching slides total 20 minutes; demo is 25 minutes: 5 code, 10 static/RViz, 5 moving/time, 5 checkpoint. Ten hidden derivation slides are outside that schedule. Use the reference sheet for deeper study instead of trying to derive all conversions live. All seven existing Week 2 files were read. The separately supplied Robotics_AutonomousSystems.pdf was not found; retain its existing printed-slide references without claiming it was reviewed. Demo code, README, RViz and teaching notes remain unchanged.
Sources:
https://docs.ros.org/en/jazzy/Concepts/Intermediate/About-Tf2.html

## Slide 2
WEEK 02 / COORDINATE FRAMES
Why do coordinates need a frame?
One physical target. Several coordinate descriptions.
Robotics & Autonomous Systems · ROS 2 Jazzy
02
x
z
y
world
x
z
y
robot
x
z
y
camera
same target
A camera measurement needs a robot-frame destination.
Notes: Timing: 1 minutes.
Visual: three labelled coordinate axes looking at one target. A frame is an origin plus axes; the target is unchanged, but its coordinates depend on that origin and basis. A camera can report a point without telling the arm where it is in robot coordinates. Ask what happens if the robot treats camera coordinates as base coordinates. Frame conversions connect sensor drivers, perception, localization and camera-guided motion. PointStamped carries both frame_id and observation time; an unlabelled three-number tuple is ambiguous. The illustration is conceptual, not a calibration of the demo camera. Do not confuse movement of a physical object with a change in its coordinate description.
Sources:
https://docs.ros.org/en/jazzy/Concepts/Intermediate/About-Tf2.html

## Slide 3
WEEK 02 / COORDINATE FRAMES
What are TF and tf2?
Geometry describes the relationship; tf2 manages it over time.
Robotics & Autonomous Systems · ROS 2 Jazzy
03
Frame
Origin + axes Where are coordinates measured?
Transform
Rotate + translate Between frames.
tf2
Time-aware library Find and apply the relationship.
Notes: Timing: 1.5 minutes.
Visual: frame, transform and tf2 cards. A coordinate frame defines an origin and three basis directions. A rigid transform gives rotation and translation between two frames. TF often refers to the ROS transform/frame system; tf2 is the library that tracks relationships over time, traverses paths, composes/inverts transforms and converts stamped data. It is not a localization or calibration algorithm: another component must supply estimated or measured relationships. The robot can have many frames and ROS nodes can publish different edges. Rigid transforms preserve distances and angles. Orientations may be stored as matrices, Euler angles or quaternions, while translation remains a separate quantity.
Sources:
https://docs.ros.org/en/jazzy/Concepts/Intermediate/About-Tf2.html

## Slide 4
WEEK 02 / COORDINATE FRAMES
Always check the conventions
Read the standard and the API before combining data.
Robotics & Autonomous Systems · ROS 2 Jazzy
04
ROS body
x forward · y left · z up
Optical
x right · y down · z forward
✓ Right-handed · m/rad ✓ Transform direction ✓ Euler sequence/axes ✓ Column/row vectors
Math q: (w, x, y, z)
ROS q: (x, y, z, w)
Notes: Timing: 2 minutes.
Visual: ROS body and optical axes plus a seven-item checklist. ROS body axes are x forward, y left, z up; optical axes are x right, y down, z forward. Both are right-handed. Metres and radians are ROS defaults; slide examples explicitly marked degrees are converted in code. Check axes/handedness, units, transform direction, fixed versus moving Euler axes and sequence, quaternion order, and row versus column vectors. This deck uses column vectors, right-handed rotations, Hamilton multiplication, fixed-axis XYZ RPY. Mathematical quaternion notation is (w,x,y,z); ROS message fields are (x,y,z,w). Parent/child is a tree relationship; target/source is the coordinate mapping requested from tf2. Different libraries and domains can use other conventions, so check their documentation; ROS has standards rather than arbitrary local choices. The demo camera_frame is simplified, not optical. Do not apply an optical correction to it without changing the actual model.
Sources:
https://github.com/ros-infrastructure/rep/blob/master/rep-0103.rst
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html

## Slide 5
WEEK 02 / COORDINATE FRAMES
Read the direction correctly
The point stays still; its coordinate tuple changes.
Robotics & Autonomous Systems · ROS 2 Jazzy
05
Ap = ARB Bp + AtB
B coordinates
A coordinates
ATB
Pose of B in A · maps B → A · same physical point
Notes: Timing: 1.5 minutes.
Define ^A T_B as the pose of frame B expressed in A. It maps coordinates written in B into coordinates written in A. ^A t_B is the B origin in A; the columns of ^A R_B are B axes written in A. Formula: p_A=R_AB p_B+t_AB. Superscript denotes destination/reference; subscript denotes source frame for T and R. A tree arrow parent→child names an edge, while the stored pose maps child coordinates→parent coordinates. For ROS lookup_transform(target,source,time), target is the destination coordinate system. Moving the frame axes changes the point coordinates without moving the physical point. Reverse the coordinate map by inverting the whole rigid transform, including the rotated translation.
Sources:
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Listener-Py.html
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp

## Slide 6
WEEK 02 / COORDINATE FRAMES
Matrix representation
Rotation preserves geometry. Translation moves the origin.
Robotics & Autonomous Systems · ROS 2 Jazzy
06
Rx(φ)
Ry(θ)
Rz(ψ)
1
0
0
0
cφ
−sφ
0
sφ
cφ
cθ
0
sθ
0
1
0
−sθ
0
cθ
cψ
−sψ
0
sψ
cψ
0
0
0
1
T =
R
t
0
1
RTR = I det R = +1
Point [p; 1] · Direction [d; 0]
Notes: Timing: 2 minutes.
Visual: three editable elementary 3×3 matrices and an editable 4×4 homogeneous block matrix. Right-hand positive rotations determine the sine signs. Use Rz(+90°)e_x=e_y as an intuitive check. A proper rotation obeys RᵀR=I and det R=+1; its nine entries have only three independent orientation degrees of freedom. R alone transforms free direction vectors. A homogeneous point [p;1] includes translation; [d;0] excludes it. T combines R with t in one matrix and ends with row 0,0,0,1. Do not read every element aloud. Highlight the z matrix and point/direction distinction; the reference sheet has every formula. These 3-vector rules are not the general transformation law for six-component twists or wrenches.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp

## Slide 7
WEEK 02 / COORDINATE FRAMES
Compose and invert
Follow the frame chain. Apply the rightmost transform first.
Robotics & Autonomous Systems · ROS 2 Jazzy
07
A
B
C
ATC = ATB BTC
T-1 =
RT
−RTt
0
1
Subtract t, then rotate back.
Notes: Timing: 1.5 minutes.
Visual: coordinate arrows C→B→A, then composition and inverse equations. T_AC=T_AB T_BC. Expanded composition is R_AC=R_AB R_BC and t_AC=R_AB t_BC+t_AB; translation from the inner frame must rotate before adding the outer translation. From p_A=Rp_B+t, subtract t, then multiply by Rᵀ. Therefore inverse translation is −Rᵀt, not simply −t. The inverse rotation is Rᵀ because a proper rotation is orthogonal. tf2 computes this chain automatically when frames are connected. The same rightmost-first ordering applies to Hamilton quaternion orientation composition. The static demo provides two edges whose composed camera-to-base result we will check later.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp
https://docs.ros.org/en/jazzy/Concepts/Intermediate/About-Tf2.html

## Slide 8
WEEK 02 / COORDINATE FRAMES
Euler angles: order matters
This lesson uses fixed-axis XYZ roll–pitch–yaw.
Robotics & Autonomous Systems · ROS 2 Jazzy
08
Roll φ
about x
Pitch θ
about y
Yaw ψ
about z
R = Rz(ψ) Ry(θ) Rx(φ)
90° x then z: ex → ey · z then x: ex → ez
Notes: Timing: 2 minutes.
Visual: roll x, pitch y, yaw z cards followed by R=Rz(ψ)Ry(θ)Rx(φ). Fixed/extrinsic XYZ means rotate about the original unmoving x, y, then z axes; matrices act rightmost first on column vectors. The equivalent intrinsic description is moving-axis ZYX with angles ψ,θ,φ. Intrinsic XYZ is different. At +90° each, RzRx e_x=e_y but RxRz e_x=e_z. Angles are convenient to read but multiple tuples can represent the same orientation. At pitch ±90° the representation is singular: roll and yaw cannot be recovered separately. This is gimbal lock in coordinates, not loss of physical rotation. Other Euler sequences require their own ordered products and inverse formulas. Use the hidden slides for expanded matrix and extraction ranges rather than deriving them during the core.
Sources:
https://github.com/ros-infrastructure/rep/blob/master/rep-0103.rst
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html

## Slide 9
WEEK 02 / COORDINATE FRAMES
Quaternion representation
An axis and angle become four constrained numbers.
Robotics & Autonomous Systems · ROS 2 Jazzy
09
q = (w, v) = (cos(α/2), k sin(α/2))
k: unit rotation axis · α: right-hand rotation angle
Unit norm
w² + x² + y² + z² = 1
ROS identity
(x, y, z, w) = (0, 0, 0, 1)
Notes: Timing: 2 minutes.
Visual: unit axis k and half-angle formula with mathematical and ROS order cards. For rotation α about unit k, scalar-first Hamilton q=(cos(α/2),k sin(α/2)). Four numbers subject to unit norm leave three orientation degrees of freedom. q and −q represent the same orientation; they are not inverse orientations. Identity is mathematical (1,0,0,0), ROS (0,0,0,1); all-zero is invalid. Normalize nonzero numerical input. Quaternions avoid the Euler singularity and interpolate well, but still require a convention and a separate translation. The demo uses α=π/2, so z=sin(π/4),w=cos(π/4); x=y=0. Field order in a message does not change mathematical multiplication if components are explicitly mapped correctly.
Sources:
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Quaternion.hpp

## Slide 10
WEEK 02 / COORDINATE FRAMES
Rotate with a quaternion
Rotate first; add translation for displaced origins.
Robotics & Autonomous Systems · ROS 2 Jazzy
10
(0, prot) = q ⊗ (0, p) ⊗ q-1
pA = prot + tAB
Unit inverse = conjugate · Composition: q_AB ⊗ q_BC
Notes: Timing: 1 minutes.
Visual: pure quaternion (0,p) → quaternion sandwich → rotated vector → add t. Under Hamilton convention, (0,p_rot)=q⊗(0,p)⊗q⁻¹. The scalar output is zero; read its vector part. For unit q, inverse is conjugate (w,−x,−y,−z). For nonunit q the general inverse divides the conjugate by squared norm. Negating all four components gives an equivalent orientation, not the inverse operation. Then p_A=p_rot+t_AB. Orientation composition follows q_AC=q_AB⊗q_BC, matching matrix order. Libraries optimize this computation; students do not need to implement the sandwich in the demo. Complete component formulas and intermediate numerical products are in the reference sheet.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Quaternion.hpp
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html

## Slide 11
WEEK 02 / COORDINATE FRAMES
One example, three representations
Same orientation. Same translation. Same base point.
Robotics & Autonomous Systems · ROS 2 Jazzy
11
Matrix
0
−1
0
1
0
0
0
0
1
Euler
RPY = (0, 0, π/2) Fixed XYZ
Quaternion
ROS (x,y,z,w): (0, 0, √2/2, √2/2)
(0.2, 0, 1) → (0, 0.2, 1.5) tz = 0.5 m
Notes: Timing: 1.5 minutes.
Visual: matrix, Euler and quaternion cards converging on the same camera→base result. static_frames.py publishes base_link→camera_mount with identity rotation and +0.5 m z translation, then camera_mount→camera_frame with zero translation and +90° rotation about z. Camera point (0.2,0,1) rotates to (0,0.2,1), then becomes base point (0,0.2,1.5). Euler is roll=0,pitch=0,yaw=π/2. Mathematical q=(√2/2,0,0,√2/2); ROS fields=(0,0,√2/2,√2/2). All three forms require the same translation. Inverse: subtract (0,0,0.5), multiply by Rᵀ, recover (0.2,0,1). Direct and composed transforms agree. Exact identifiers and values come from demo/static_frames.py and demo/transform_point.py. The camera is simplified rather than optical. The reference sheet shows the full homogeneous matrix and intermediate quaternion products.
Sources:
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html

## Slide 12
WEEK 02 / COORDINATE FRAMES
The frame tree
Frames are coordinate systems; ROS nodes publish their relationships.
Robotics & Autonomous Systems · ROS 2 Jazzy
12
world
base_link
camera_mount
camera_frame
dynamic · moving_base
static · static_frames
One parent per child · one authority per edge · no cycles
Disconnected trees have no transform path.
Notes: Timing: 1 minutes.
Visual: world→base_link→camera_mount→camera_frame. Arrows here mean parent→child relationship, not coordinate mapping direction. moving_base publishes the dynamic world→base_link edge; static_frames publishes both static camera/base edges. A frame is not a node: one node can publish several frames and several nodes can collectively supply a tree. A child has one parent at a time; avoid cycles. Give each edge one authoritative broadcaster; conflicting broadcasters produce inconsistent data, not useful consensus. Multiple disconnected trees can exist, but lookup cannot cross roots without a connecting edge. Demo world is a generic reference; it does not implement REP 105 map/odom localization. The sensor-to-base chain remains static even when the base moves in world.
Sources:
https://docs.ros.org/en/jazzy/Concepts/Intermediate/About-Tf2.html
https://github.com/ros-infrastructure/rep/blob/master/rep-0105.rst

## Slide 13
WEEK 02 / COORDINATE FRAMES
How tf2 works
Publish edges. Buffer samples. Look up a connected path.
Robotics & Autonomous Systems · ROS 2 Jazzy
13
static_frames
/tf_static
moving_base
/tf
Listener + Buffer
Lookup
Several publishers · each listener has its own buffer
Notes: Timing: 1 minutes.
Visual: static_frames and moving_base feed /tf_static and /tf, then listener/buffer and lookup. StaticTransformBroadcaster uses durable static data suitable for late listeners; TransformBroadcaster streams dynamic samples. TransformStamped includes header.frame_id parent, child_frame_id child, timestamp, translation and quaternion. Several nodes can publish different edges. Each TransformListener populates its own Buffer; there is no central lookup server. DDS transports samples between endpoints; executor callbacks consume them and fill the buffer. Lookup then performs geometry and time selection locally. These responsibilities are distinct. In the scripts, point_transformer creates Buffer and TransformListener, receives data while spinning, and calls lookup in its timer. Static data is time-independent, but publisher lifetime matters for late discovery; leave the existing static script spinning.
Sources:
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Static-Broadcaster-Py.html
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Listener-Py.html

## Slide 14
WEEK 02 / COORDINATE FRAMES
Transform at the measurement time
A moving robot makes an old observation different from a new one.
Robotics & Autonomous Systems · ROS 2 Jazzy
14
Observation at tₘ
Now
Use the transform at tₘ.
Latest is not acquisition time.
Finite history · consistent clocks · preserve the stamp
Notes: Timing: 1 minutes.
Visual: acquisition time and current time on a timeline. Time() requests latest common usable transform, not necessarily now. Real observations need the transform at their acquisition timestamp when the chain is dynamic. The demo camera-to-base relationship is static, so latest lookup there is valid. moving_base adds time dependence only between world and base_link. transform_point.py restores the input stamp after do_transform_point, so RViz can convert both point messages into world at the same measurement time. The synthetic point stays fixed in camera coordinates and moves with the robot; a real world-fixed target would change its camera coordinates. History is finite; requests too old or newer than buffered dynamic samples raise extrapolation. Missing frames and disconnected paths fail too. Match clock sources and use_sim_time; bounded waiting/retry can allow data to arrive, while blocking the only executor thread may prevent listener callbacks. Existing code does not simulate delayed camera observations.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/src/cache.cpp
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Listener-Py.html

## Slide 15
WEEK 02 / COORDINATE FRAMES
Inspect and predict
Different coordinate tuples should overlap in RViz.
Robotics & Autonomous Systems · ROS 2 Jazzy
15
ros2 run tf2_ros tf2_echo base_link camera_frame
ros2 run tf2_ros tf2_echo world base_link
lookup_transform(target, source, time)
RViz Fixed Frame: base_link → world
Notes: Timing: 1 minutes.
Visual: tf2_echo commands, lookup target/source labels and RViz fixed-frame badge. ros2 run tf2_ros tf2_echo base_link camera_frame shows camera pose in base, matching lookup_transform('base_link','camera_frame',Time()). Reverse arguments reverse the mapping. RViz starts Fixed Frame=base_link; switch to world after moving_base runs. The blue camera point and orange base point differ numerically but coincide physically. Start point_transformer before static_frames for a recoverable missing-frame warning: the timer catches TransformException, returns without blocking, and retries on later ticks while listener callbacks fill the buffer. Also inspect ros2 interface show geometry_msgs/msg/TransformStamped and topic endpoints using the existing README. The demo code publishes /point_camera and /point_base. Sources include the unchanged demo/README.md; classroom command execution is separate from deck generation checks.
Sources:
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Debugging-Tf2-Problems.html
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Listener-Py.html

## Slide 16
WEEK 02 / COORDINATE FRAMES
Live demo: read, run, predict
Keep the geometry and timestamps in view.
Robotics & Autonomous Systems · ROS 2 Jazzy
16
world
base_link
camera_mount
camera_frame
dynamic · moving_base
static · static_frames
Camera (0.2, 0, 1) → Base (0, 0.2, 1.5)
Predict: missing frame? moving base? old timestamp?
Notes: Timing: 25 minutes.
5 minutes CODE: read static_frames.py, transform_point.py, moving_base.py. Identify node names static_frames, point_transformer, moving_base; parent/child fields, ROS quaternion order, broadcaster types, Buffer/TransformListener, timer callbacks, spin and cleanup. Explain static latest lookup, TransformException recovery, do_transform_point and restored input stamp. 10 minutes STATIC/RVIZ: follow existing README commands unchanged. Source Jazzy and existing ROS_DOMAIN_ID=42/localhost setup in each terminal. Start point node before static broadcaster; observe recovery. Echo base_link camera_frame, open RViz with existing config, inspect point topics and message definition. Camera (0.2,0,1) becomes base (0,0.2,1.5); points overlap. Explain frame/node distinction and late-listener static data. 5 minutes MOVING/TIME: run moving_base.py, echo world base_link, switch RViz fixed frame to world. Yaw=0.2·elapsed radians; timer=0.1 s (10 Hz). Ask why world point moves but base coordinates stay constant. Synthetic point moves with camera. Explain measurement-time world conversion, unavailable history, clock mismatch and wait/retry; this is not a delayed-image demo. 5 minutes CHECKPOINT: select lookup target/source, predict inversion and rotation order, check optical/body axes and quaternion order, explain frames/transforms/tf2. Recap and questions. Keep hidden derivations outside this 45-minute session. Existing professor PDF reference retained, not reviewed.
Sources:
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Writing-A-Tf2-Listener-Py.html
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Debugging-Tf2-Problems.html

## Slide 17
OPTIONAL / DEEPER DISCUSSION
Expanded Euler rotation matrix
Fixed XYZ / column vectors: R = Rz(ψ) Ry(θ) Rx(φ)
Robotics & Autonomous Systems · ROS 2 Jazzy
17
cψcθ
cψsθsφ − sψcφ
cψsθcφ + sψsφ
sψcθ
sψsθsφ + cψcφ
sψsθcφ − cψsφ
−sθ
cθsφ
cθcφ
c = cos(angle) · s = sin(angle) · full angles here
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. In these entries c and s mean full-angle cosine and sine, unlike the half-angle notation on the quaternion conversion slide. Derive by multiplying RyRx first, then premultiplying Rz. This is specifically fixed XYZ RPY, equivalent to intrinsic ZYX; different sequences require different products. All nine entries and elementary matrices appear in TF_MATH_REFERENCE.md. Test RᵀR=I and det R=1, then compare the expanded matrix to elementary-matrix multiplication and quaternion conversion. Avoid checking rounded display entries at very tight tolerance.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp

## Slide 18
OPTIONAL / DEEPER DISCUSSION
Recover Euler angles
Away from the singularity, recover one principal representative.
Robotics & Autonomous Systems · ROS 2 Jazzy
18
θ = atan2(−r31, √(r11² + r21²))
φ = atan2(r32, r33) ψ = atan2(r21, r11)
θ ∈ [−π/2, π/2] · φ, ψ ∈ (−π, π]
cos θ ≈ 0: φ = 0, ψ = atan2(−r12, r22)
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. For fixed XYZ RPY use pitch=atan2(−r31,sqrt(r11²+r21²)), roll=atan2(r32,r33), yaw=atan2(r21,r11). Principal pitch lies in [−π/2,π/2], roll/yaw in (−π,π] with consistent boundary handling. At cos(pitch)≈0 set roll=0 and yaw=atan2(−r12,r22); pitch retains its atan2 value. At +90° only yaw−roll is identifiable; at −90° yaw+roll. Roll30/yaw45 at pitch+90 reconstructs with roll0/yaw15; at −90 reconstructs with roll0/yaw75. This is a coordinate singularity. Reconstruct and compare matrices rather than assuming Euler angles are unique. Reference sheet includes singular branch and examples.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp

## Slide 19
OPTIONAL / DEEPER DISCUSSION
Quaternion → rotation matrix
Unit Hamilton quaternion q = (w, x, y, z).
Robotics & Autonomous Systems · ROS 2 Jazzy
19
1 − 2(y²+z²)
2(xy−wz)
2(xz+wy)
2(xy+wz)
1 − 2(x²+z²)
2(yz−wx)
2(xz−wy)
2(yz+wx)
1 − 2(x²+y²)
Normalize first · R(q) = R(−q) · ROS order is xyzw
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. The full editable matrix uses mathematical scalar-first q and column-vector right-hand rotations. Normalize nonzero q first; all-zero is invalid. Each entry is quadratic, so negating all four components preserves R. Check identity and ±90° rotations about each axis, then a mixed-axis example. Cross-check against independently multiplied elementary matrices. Orthogonality and determinant tests check that conversion yields SO(3), not merely a plausible set of entries. The scalar-first formulas must not be applied to a raw xyzw array without reordering named components. Reference sheet contains the complete formula.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html

## Slide 20
OPTIONAL / DEEPER DISCUSSION
Stable matrix → quaternion
Choose the largest component; stay stable near 180°.
Robotics & Autonomous Systems · ROS 2 Jazzy
20
aw = (1+r11+r22+r33)/4
ax = (1+r11−r22−r33)/4
ay = (1−r11+r22−r33)/4
az = (1−r11−r22+r33)/4
Take √(largest), recover the others, then normalize.
180° about x: (a_w,a_x,a_y,a_z) = (0,1,0,0)
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. Compute aw=(1+r11+r22+r33)/4, ax=(1+r11−r22−r33)/4, ay=(1−r11+r22−r33)/4, az=(1−r11−r22+r33)/4. Choose largest, take positive square root, recover others, normalize. If w largest: x=(r32−r23)/(4w), y=(r13−r31)/(4w), z=(r21−r12)/(4w). If x largest: w=(r32−r23)/(4x), y=(r12+r21)/(4x), z=(r13+r31)/(4x). If y largest: w=(r13−r31)/(4y), x=(r12+r21)/(4y), z=(r23+r32)/(4y). If z largest: w=(r21−r12)/(4z), x=(r13+r31)/(4z), y=(r23+r32)/(4z). At 180° about x candidates=(0,1,0,0), q=(0,1,0,0). Validate R first; only clamp tiny negative roundoff. Avoid trace-only division by w near zero. q or −q may be returned; compare reconstructed R. All branches in reference.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp

## Slide 21
OPTIONAL / DEEPER DISCUSSION
Roll–pitch–yaw → quaternion
Fixed XYZ only; c and s here use HALF angles.
Robotics & Autonomous Systems · ROS 2 Jazzy
21
w = cφ cθ cψ + sφ sθ sψ
x = sφ cθ cψ − cφ sθ sψ
y = cφ sθ cψ + sφ cθ sψ
z = cφ cθ sψ − sφ sθ cψ
Reverse: normalized q → R(q) → Euler (singular branch)
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. Here cφ=cos(φ/2),sφ=sin(φ/2), and similarly θ,ψ. Derive scalar-first q=qz(ψ)⊗qy(θ)⊗qx(φ). Components: w=cφcθcψ+sφsθsψ; x=sφcθcψ−cφsθsψ; y=cφsθcψ+sφcθsψ; z=cφcθsψ−sφsθcψ. These are not universal for intrinsic XYZ or another Euler sequence. Convert radians correctly. Reverse: normalize quaternion, build R(q), recover Euler with singular handling. ROS message fields take x,y,z,w from these named components; message layout does not change this algebra. Reference sheet includes derivation and reverse conversion.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Quaternion.hpp
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html

## Slide 22
OPTIONAL / DEEPER DISCUSSION
Quaternion algebra
Hamilton multiplication; order and multiplication side matter.
Robotics & Autonomous Systems · ROS 2 Jazzy
22
q1 ⊗ q2 = (w1w2 − v1·v2,
w1v2 + w2v1 + v1×v2)
q* = (w, −v) q-1 = q* / ‖q‖²
qrel = q2 ⊗ q1-1 R(q) = R(−q)
Unit norm: inverse = conjugate. Sign flip ≠ inverse.
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. Product (w1,v1)⊗(w2,v2)=(w1w2−v1·v2,w1v2+w2v1+v1×v2). Expanded components and all signs are in the reference. Conjugate=(w,−v); general inverse=q*/norm², unit inverse=q*. Composition qAC=qAB⊗qBC follows matrix order. If q2=qrel⊗q1 with both in the same reference, relative qrel=q2⊗q1⁻¹. Negating all four entries gives an equivalent orientation, not inverse; conjugating changes orientation to inverse except special cases. Verify sandwich rotation against R(q), norm of product, inverse-to-identity and R(q)=R(−q).
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Quaternion.hpp
https://docs.ros.org/en/jazzy/Tutorials/Intermediate/Tf2/Quaternion-Fundamentals.html

## Slide 23
OPTIONAL / DEEPER DISCUSSION
Conventions change the formula
Define the operation and vector layout before copying equations.
Robotics & Autonomous Systems · ROS 2 Jazzy
23
Active
Rotate the vector: p′ = Rp
Passive
Reverse basis map: use Rᵀ
Row vectors: p′T = pTRT + tT
Basis change: Rnew = SA Rold SB-1
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. Active rotation physically rotates a vector in a fixed basis p'=Rp; passive basis change expresses the same vector in rotated axes, using inverse/transpose relative to that basis orientation. Define source/target explicitly. Row-vector form is p'ᵀ=pᵀRᵀ+tᵀ and homogeneous matrix Tᵀ; transposition reverses multiplication order. If pnew=S pold with same basis conversion both sides, Rnew=S Rold S⁻¹, tnew=S told. For distinct source/target changes Rnew=SA Rold SB⁻¹, tnew=SA told. A reflection changing handedness cannot itself be encoded by a unit quaternion. Fixed XYZ matches intrinsic ZYX with reversed angles; other sequences require ordered products appropriate to that convention. Reference section on conventions expands these cases.
Sources:
https://github.com/ros-infrastructure/rep/blob/master/rep-0103.rst

## Slide 24
OPTIONAL / DEEPER DISCUSSION
ROS axes and common frames
Body and optical conventions coexist in one robot.
Robotics & Autonomous Systems · ROS 2 Jazzy
24
Body
x forward · y left · z up
Optical
x right · y down · z forward
map → odom → base_link → sensor
map: corrections may jump · odom: continuous, drifts
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. REP103 body axes: x forward,y left,z up; optical: x right,y down,z forward. For aligned axes the coordinates convert p_opt=(−y_body,−z_body,x_body), using S=[[0,−1,0],[0,0,−1],[1,0,0]]. This is a convention example, not an extra edge in our simplified demo. REP105 map is a long-term world reference, typically drift-bounded but may jump after corrections; odom is continuous but can drift; base_link is attached to the robot. Common tree map→odom→base_link→sensor separates corrections from smooth odometry. Our world is generic and no localization node estimates map/odom. Names alone do not guarantee semantics: check the actual publisher and documentation.
Sources:
https://github.com/ros-infrastructure/rep/blob/master/rep-0103.rst
https://github.com/ros-infrastructure/rep/blob/master/rep-0105.rst

## Slide 25
OPTIONAL / DEEPER DISCUSSION
Interpolate time and orientation
Use compatible buffered samples; choose the short quaternion arc.
Robotics & Autonomous Systems · ROS 2 Jazzy
25
u = (τ−τ0)/(τ1−τ0) t(u) = (1−u)t0 + ut1
q(u) = [sin((1−u)Ω)/sin Ω] q0
+ [sin(uΩ)/sin Ω] q1
Ω = acos(q₀·q₁) · flip q₁ if dot < 0 Near equality: normalize the linear blend.
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. With timestamps τ0,τ1 and τ between them, u=(τ−τ0)/(τ1−τ0). Translation interpolates linearly t(u)=(1−u)t0+ut1. For unit q0,q1, if their dot is negative replace q1 by its equivalent −q1. Clamp dot to [−1,1] before acos; Ω=acos(dot). SLERP uses sin((1−u)Ω)/sinΩ and sin(uΩ)/sinΩ weights. Near equality use normalized linear blending to avoid a small denominator. q1=−q0 represents no physical rotation after sign choice. Endpoints and norms should check correctly. tf2 interpolates buffered compatible dynamic samples; unavailable past/future still raises extrapolation and static edges remain constant. Interpolation is an approximation of motion, not arbitrary extrapolation. Reference includes full formula and sign discussion.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/src/cache.cpp
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Quaternion.hpp

## Slide 26
OPTIONAL / DEEPER DISCUSSION
Worked mathematical checks
Compare physical transforms, not raw angle tuples or quaternion signs.
Robotics & Autonomous Systems · ROS 2 Jazzy
26
0.664463
−0.733295
0.144110
0.664463
0.491450
−0.562997
0.342020
0.469846
0.813798
RPY: (30°, −20°, 45°) Fixed XYZ
q ≈ (0.861642, 0.299673, −0.057422, 0.405550)
Round trip · q / −q · near 180° · singular Euler
Notes: Timing: 0 minutes. Hidden optional reference, outside the 45-minute lesson.
Untimed backup. Mixed fixedXYZ RPY=(30°,−20°,45°) gives math q≈(0.861642,0.299673,−0.057422,0.405550); full R is on slide and in reference. Point (1,2,3) rotates to approximately (−0.369798,−0.041628,3.723106); adding (0.4,−0.2,0.7) gives (0.030202,−0.241628,4.423106). Inverse recovers original using unrounded values. Demo forward: (0.2,0,1)→(0,0.2,1.5) and back. Noncommuting +90° x/z rotations send e_x to e_y or e_z depending on order. Test identity, ±90° axes, mixed axes, direct/composed transform, RᵀR=I, det=1, unit quaternion, q/−q same matrix, largest-component conversion near/exact180°, singularEuler reconstruction and SLERP. Run validate_math.ps1. Classroom ROS/RViz execution is separate from these slide-generation/math checks.
Sources:
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Matrix3x3.hpp
https://github.com/ros2/geometry2/blob/jazzy/tf2/include/tf2/LinearMath/Quaternion.hpp