## Slide 1
WEEK 04 / CONFIGURATION SPACE & PRM
Configuration space & PRM
Describe the whole robot. Find a collision-free route.
Robotics & Autonomous Systems · Motion Planning
01
x
y
q₁ (rad)
π
−π
q₂
20 min concepts · 25 min demo
Illustrative roadmap
Notes: TIMING: 0 minutes. Untimed title. Week 4 learns configuration space and probabilistic roadmaps using the existing Python-only arm demo. Audience knows ROS, frames, simulation and planar FK/IK from Weeks 1–3. No ROS or Gazebo process is needed this week. Teaching slides total 20 minutes; demo is 25 minutes: 5 code, 12 reveal stages and animate, 8 sample-count comparison and checkpoint. Five hidden backups are untimed. Incorporate the former separate recap into motivation, not an additional five-minute block. All nine existing Week 4 files were read; preserve the teaching notes, README, four Python files and two overview PNGs. The separate MotionPlaningIntroPRM.pdf was not found in workspace/parent and was not reviewed; preserve its existing Oren Salzman references by section/printed number. Main diagram vertices are clearly labelled illustrative, not the seed-7 demo samples. Use saved actual overview for the demo transition and comparisons.
SOURCES
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 2
WEEK 04 / CONFIGURATION SPACE & PRM
Why motion planning?
A reachable goal does not guarantee a clear route.
Robotics & Autonomous Systems · Motion Planning
02
Start: free
q = (−0.7, 0.6)
Midpoint: collision
q = (0, 0)
Goal: free
q = (0.7, −0.6)
Notes: TIMING: 1 minutes. Visual: the same two-link arm in safe start, colliding intermediate pose and safe goal. Week 3 IK found a configuration for a desired tool point; it did not check how to move there. Motion planning seeks a continuous route through allowed configurations while respecting collision constraints along the way. Use exact start (−.7,.6), goal (.7,−.6) radians and their linear midpoint (0,0). The endpoints are free under the demo geometry, but the straight arm at the midpoint crosses the obstacle. This is a need for a detour, not evidence the goal is unreachable. Use the same lengths .6/.4 m; obstacle center (.8,0), radius .12. Pose diagrams use physical link thickness .03 m radius and the obstacle padding outline .01 m. Planning here is geometric in a static known scene, not dynamic control, acceleration limits or robust physical execution.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 3
WEEK 04 / CONFIGURATION SPACE & PRM
Three kinds of planning
Choose actions, search connections, and realize robot motion.
Robotics & Autonomous Systems · Motion Planning
03
Task planning
Approach → grasp → place Choose actions.
Graph search
Find a route among known connections.
Motion planning
Move the whole robot without collision.
PRM builds geometric connections, then searches them.
Notes: TIMING: 2 minutes. Visual: equal-sized task planning, graph search and motion planning cards, linked to one pick-and-place task. Task planning chooses actions and their order, e.g. approach, grasp and place with preconditions/effects. Graph search finds a route among specified vertices and edges under costs; a graph by itself does not know robot geometry. Motion planning finds continuous joint configurations connecting poses without collision in the full robot model. PRM builds a graph approximation in continuous configuration space, then uses graph search. These are complementary levels/tools, not mutually exclusive categories or a claim that every other planner is discrete. A symbolic task can be feasible abstractly but require geometric checking; a graph route can be invalid if its robot motions were never validated. Deeper task-and-motion planning integration belongs to Week 5. The main demo compares geometric paths, not pick/grasp symbolic operations.
SOURCES
https://arxiv.org/abs/2010.01083
https://www.cs.cmu.edu/~motionplanning/papers/sbp_papers/PRM/prmbasic_01.pdf

## Slide 4
WEEK 04 / CONFIGURATION SPACE & PRM
Workspace versus configuration space
One point in configuration space represents the whole arm.
Robotics & Autonomous Systems · Motion Planning
04
Workspace · metres
x
y
Links: 0.6 m + 0.4 m
q₁ (rad)
π
−π
q₂
↔
q = (−0.7, 0.6) rad
Notes: TIMING: 2 minutes. Visual: editable workspace arm at start (−.7,.6), connected to one highlighted point in a q1/q2 square. Workspace is the physical xy plane in metres, containing robot and circular obstacle. Configuration is q=(q1,q2) in radians; FK determines base, elbow and tip. The tool xy point alone does not specify the whole configuration: Week 3 showed two IK solutions can have the same tool position. This robot has two independent revolute joint coordinates, so its configuration space is two-dimensional even though every arm pose contains multiple points. q2 is relative to link1. Hard limits give C=[−π,π]² and opposite boundaries are not connected by wrapping. An unrestricted 2R model has a toroidal S1×S1 topology and needs a different metric/interpolator. Grid coloring is an approximate teaching display; geometric predicates decide free configurations. Briefly identify start/goal but delay revealing the demo's actual final route.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 5
WEEK 04 / CONFIGURATION SPACE & PRM
Obstacles become invalid configurations
Check the robot geometry, not only its end effector.
Robotics & Autonomous Systems · Motion Planning
05
x
y
Tip is clear. Link 2 collides.
q₁ (rad)
π
−π
q₂
Blocked region: approximate
Notes: TIMING: 1.5 minutes. Visual: colliding straight arm at q=(0,0) and the corresponding point in the blocked configuration-space region. The physical obstacle is a circle centered (.80,0), radius .12 m. The whole arm can collide even if its tool is clear. Use FK to place both link segments and test each capsule of radius .03 m. Add .01 m padding; contact with the padded model is rejected. Define C_free as allowed configurations passing the geometry query, and C_obs as invalid ones under that model. Obstacle shapes in configuration space are generally not the same as their workspace shape: here a circle creates a coupled curved region in two angles. The displayed native grid is coarser than the demo display and explicitly approximate; the planner does not search that raster. The collision predicate, not a colored pixel, is the source of truth. Self-collision is intentionally outside this simplified model.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 6
WEEK 04 / CONFIGURATION SPACE & PRM
Safe endpoints, blocked motion
A valid vertex does not make every outgoing motion valid.
Robotics & Autonomous Systems · Motion Planning
06
q₁ (rad)
π
−π
q₂
q(s) = (1−s)qstart + sqgoal
s = 0, 1: free
s = ½: collision
A valid motion needs valid intermediate configurations.
Notes: TIMING: 1.5 minutes. Visual: the straight start→goal segment through the blocked C-space region, endpoints in teal and midpoint in red. Linear local motion q(s)=(1−s)a+sb for s in [0,1]. Both endpoints are free, but s=.5 gives (0,0), which collides. edge_free tests configurations produced by interpolate, including endpoints. This motivates a separate edge predicate, not checking only vertices. For the demo, n=max(1,ceil(max(|b1−a1|,|b2−a2|)/.01)); evaluate i/n for i=0..n. Here max joint change is 1.4 rad, so n=140 and 141 configurations are checked if not short-circuited. This is sampled checking, not a general continuous collision detector. Padding adds geometric clearance but is not a guarantee for arbitrary resolution/model changes or physical robot operation. Right panel distinguishes free(a),free(b) from edge_free(a,b).
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 7
WEEK 04 / CONFIGURATION SPACE & PRM
PRM: build, query, verify
The live demo will make these steps clearer.
Robotics & Autonomous Systems · Motion Planning
07
1
Sample
2
Filter
3
Neighbors
4
Validate
5
Store graph
6
Attach query
7
Search
8
Verify
Build once → reuse for many start–goal queries.
Notes: TIMING: 1 minutes. Visual: eight-step editable flow: sample, filter, neighbors, validate motions, store graph, attach query, search, verify. PRM stands for Probabilistic Roadmap. Construction builds a reusable graph of collision-free configurations and locally valid motions. Query attaches the actual start/goal, which need not be sampled vertices, and searches. Verification inspects the returned segments under the model; it does not create a physical execution guarantee. Main slides now unpack every step with Implement/Check cues; the live demo maps them to functions and reveals samples, edges and route separately. The demo prepares its computation at startup, so staged reveals are not incremental recomputation. Ordinary PRM is introduced; no claim of PRM* optimality or a completeness theorem for this exact fixed-k implementation. Use the original paper as background and the local source for implementation specifics.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
https://www.cs.cmu.edu/~motionplanning/papers/sbp_papers/PRM/prmbasic_01.pdf
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 8
WEEK 04 / CONFIGURATION SPACE & PRM
1 · Sample configurations
Draw joint-angle pairs inside the allowed configuration space.
Robotics & Autonomous Systems · Motion Planning
08
q₁ (rad)
π
−π
q₂
Attempts ≠ accepted samples
Implement
Seeded uniform angles; bounded attempts.
Check
Limits, repeatability, attempt exhaustion.
Notes: TIMING: 1.5 minutes. Visual: illustrative random candidates in C-space. Implement build_roadmap uses random.Random(seed), two uniform draws in [−π,π], and a rejection loop until the requested accepted count is reached. Defaults: 300 accepted samples, k=10, seed=7. Attempts include rejected candidates; 300 samples does not mean 300 random draws. Default max attempts=100*samples total, overridden by the Python max_attempts keyword. Exhaustion raises RuntimeError with the accepted count. A fixed seed makes the sample sequence reproducible, not elapsed timings. The actual seed-7 runs documented in README accepted 20 in 21 attempts and 300 in 312. The schematic slide samples use a separately labelled illustrative set rather than claiming to match Python's generator. Tests: finite two-angle values within limits, same seed/settings reproduce points, the 20-sample sequence is a prefix of 300, and mocked always-collision exhaustion terminates. Existing tests cover determinism/prefix and bounded failure.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 9
WEEK 04 / CONFIGURATION SPACE & PRM
2 · Keep free configurations
Forward kinematics supplies the geometry for collision checks.
Robotics & Autonomous Systems · Motion Planning
09
clearance(q) > 0.01 m
Thickness + padding matter.
Implement
FK → both link capsules → clearance.
Check
Either link, contact, and known poses.
Notes: TIMING: 1.5 minutes. Visual: rejected straight configuration and the collision-clearance predicate. forward_points returns base=(0,0), elbow=(.6cosq1,.6sinq1), tip=elbow+(.4cos(q1+q2),.4sin(q1+q2)). segment_distance projects the obstacle center onto each segment, clamps projection to [0,1] and handles zero-length segments. clearance is the minimum segment-center distance minus obstacle radius and link radius. configuration_free requires clearance>PADDING; equality/contact fails. No need to explicitly construct every C-space obstacle boundary: use a predicate on queried configurations. Tests: actual start/goal free, zero collides; patch obstacles to hit link1 or link2; padded contact rejected; invalid length/nonfinite/out-of-limit q fails validation. Full derivation is in backup notes. This predicate models the full link geometry rather than checking only the tool.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 10
WEEK 04 / CONFIGURATION SPACE & PRM
3 · Choose nearby candidates
Distance proposes a connection; geometry decides whether to keep it.
Robotics & Autonomous Systems · Motion Planning
10
q₁ (rad)
π
−π
q₂
d(q,a) = ‖q−a‖₂
Implement
Sort joint-space distance; exclude self.
Check
Known ordering; fewer than k vertices.
Notes: TIMING: 1 minutes. Visual: a highlighted configuration and candidate neighbor lines in an illustrative graph. nearest sorts (math.dist(q,p),index) tuples and takes the first k, excluding the requested self-index. Distance is Euclidean in this bounded angle-coordinate square, d=√((Δq1)²+(Δq2)²), with values in joint-space radians. Do not wrap opposite boundaries; do not use tool-space distance for this demo. Default k=10; a small roadmap can provide fewer candidates. Neighbor sets are not necessarily symmetric, but the construction considers the union: a pair is considered if either endpoint selects the other. A candidate line remains untrusted until edge_free. The schematic highlights four candidates for readability; the actual demo uses k=10. Checks: toy points with known distances/order, tie handling by index, self excluded, fewer than k returns available vertices. Changing sample count can change neighbors and edges even when sample points form a prefix. Candidate connections drawn dashed, not as already-valid edges.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 11
WEEK 04 / CONFIGURATION SPACE & PRM
4 · Validate local motions
Inspect configurations along the connection, including endpoints.
Robotics & Autonomous Systems · Motion Planning
11
q₁ (rad)
π
−π
q₂
≤ 0.01 rad per joint per step
Implement
Interpolate; check every sampled pose.
Check
Blocked midpoint; endpoint inclusion.
Notes: TIMING: 1.5 minutes. Visual: a candidate crossing the blocked region, interpolation dots that turn red at invalid poses. interpolate validates both endpoints and positive finite step. n=max(1,ceil(max coordinate change/step)), returned list includes n+1 configurations and each coordinate increment is at most 0.01 rad. edge_free short-circuits if any configuration fails. This linear motion stays within the convex hard-limit square but can cross obstacle regions. Padding is 0.01 m and physical link radius 0.03 m; both matter independently of angle-step units. Checks: free endpoints with colliding midpoint return False; endpoints included; coordinate increments bounded; a known clear segment passes; invalid steps rejected; no artificial wrapping from −3 to +3. Independent denser replay is useful to detect implementation errors, but no finite sampled test is a universal continuous-collision certificate. Do not claim a controller trajectory is produced.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 12
WEEK 04 / CONFIGURATION SPACE & PRM
5 · Store the roadmap
Configurations become vertices; validated motions become edges.
Robotics & Autonomous Systems · Motion Planning
12
q₁ (rad)
π
−π
q₂
wab = ‖qa−qb‖₂
Implement
Undirected adjacency; length weights.
Check
Symmetry, costs, no duplicate edges.
Notes: TIMING: 1 minutes. Visual: a small editable roadmap with the edge-weight formula, with invalid candidate edges omitted. Roadmap holds points, adjacency, neighbors, attempts and build seconds. connect skips self-edges and existing edges, then runs edge_free. Only after success does it append both (a,b) and (b,a) with identical weight math.dist(q_a,q_b). Construction uses an examined set of sorted index pairs so a pair selected from either endpoint is checked once. Vertex denotes the entire arm; edge denotes the proposed local interpolation, not a free arbitrary shortcut between safe points. Check adjacency symmetry, positive/nonnegative appropriate weights, expected Euclidean values, no duplicates/self-edges, and each stored edge passing geometric validation. Reported edge_count=sum(degrees)//2 counts undirected preprocessing edges; query attachments are additional. Graph may have multiple connected components. Preprocessing can be reused only while model, obstacles and validity assumptions remain unchanged.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
https://www.cs.cmu.edu/~motionplanning/papers/sbp_papers/PRM/prmbasic_01.pdf

## Slide 13
WEEK 04 / CONFIGURATION SPACE & PRM
6 · Use an unsampled point
Add the actual start or goal; connect it without snapping.
Robotics & Autonomous Systems · Motion Planning
13
qnew
valid
rejected
Orange dashed: candidate
Implement
Validate endpoint; copy; add; connect.
Check
Exact endpoint retained; original unchanged.
Notes: TIMING: 1 minutes. Dedicated slide. Visual: an editable configuration-space roadmap with blue sampled vertices, orange q_new, dashed orange candidate connection, rejected red connection across C_obs and retained teal valid attachments. The illustrated q_new is the actual start (−0.7,0.6), absent from the illustrative vertex set. Unsampled means not already a sampled vertex, not outside the allowed angle bounds. First validate joint limits and collision status. query_roadmap copies points and each adjacency row, adds the actual start and goal to that query copy, selects their k nearest preprocessing vertices, checks each entire local motion via connect/edge_free, and stores only valid weighted connections. It also considers a checked direct start→goal edge. Never snap to a neighbor or assume the nearest edge is valid. Apply the procedure to both endpoints. Search from actual start index to actual goal index. Failure to attach or find a route is failure in this graph, not proof of no physical route. Tests: endpoint not in sample set retained exactly, original graph unchanged, invalid endpoint rejected, failed/disconnected attachment returns empty path/None length, free equal endpoints gives one point/zero length. Clicking the GUI only previews a pose; it does not run a new query. Show endpoint attachment through code without changing GUI behavior.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 14
WEEK 04 / CONFIGURATION SPACE & PRM
7 · Search the graph
Dijkstra finds a minimum-cost route among the validated edges.
Robotics & Autonomous Systems · Motion Planning
14
1
1
5
0
1
2
3
isolated
0 → 1 → 2: total cost 2
Implement
Heap frontier + costs + parent links.
Check
Known shortest route; disconnected graph.
Notes: TIMING: 1 minutes. Visual: an editable tiny graph with edge costs 1, 1, 5. The shortest 0→2 route is 0→1→2, cost 2, rather than direct cost 5; isolated vertex 3 is unreachable. shortest_path maintains a min-heap of tentative costs, skips stale entries, relaxes outgoing edges, records parent links and reconstructs the route when goal is removed at its minimum cost. Weights in the actual roadmap are nonnegative joint-space Euclidean lengths. Dijkstra does not decide whether a robot link collides: that was edge validation's responsibility. Shortest means shortest under these graph weights, not globally shortest in C_free, least tool travel distance or fastest motion. Tests use the exact small graph from test_demo.py, disconnected target and equal start/goal; compare returned indices and summed cost. A* is a later/course-homework alternative, not another planner to add here.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 15
WEEK 04 / CONFIGURATION SPACE & PRM
8 · Verify the returned path
Check endpoints, segments, and cost before interpreting playback.
Robotics & Autonomous Systems · Motion Planning
15
q₁ (rad)
π
−π
q₂
Replay more densely: 0.002 rad
Implement
Replay segments; sum joint-space lengths.
Check
Endpoints, clearance, and reported cost.
Notes: TIMING: 1 minutes. Visual: highlighted valid illustrative detour in C-space; use the demo to show the corresponding arm poses. Verify exact first/last configurations, finite in-limit values, every polyline segment with edge_free, and sum of segment distances equal returned length. Independently denser sampling (0.002 rad in the existing test) and a separately formulated NumPy distance calculation check physical clearance of both links. This strengthens testing but remains sampled/model-dependent. demo playback is assembled using interpolate and follows the validated polyline; speed 0.7 joint-space rad/s is illustrative timing, not actuator/acceleration modeling. Synchronizing workspace arm and C-space marker reinforces one configuration=whole robot. GUI click pauses/resets playback and previews a configuration; it does not replan. The actual large-demo final path is reserved for the live demo transition to preserve predictions.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Demo source: demo/planner.py and demo/test_demo.py
Demo source: demo/demo.py and demo/README.md

## Slide 16
WEEK 04 / CONFIGURATION SPACE & PRM
Interpret success and failure
A finite roadmap can miss a route that physically exists.
Robotics & Autonomous Systems · Motion Planning
16
20 samples · seed 7
91 edges Path length: 5.630 rad
300 samples · seed 7
1,728 edges Path length: 5.243 rad
Both found a route in the documented TA run.
More samples can help; success and better cost are not guaranteed.
Notes: TIMING: 1.5 minutes. Visual: equal-size sparse/denser comparison cards with the actual README numbers. Uniform sampling can miss narrow passages; limited candidate connections can leave components disconnected. No path found in this roadmap means exactly that graph had no route, not impossibility of robot motion. For fixed seed 7 and k=10, documented 20 samples: 21 attempts, 91 construction edges, length ≈5.630 rad; 300: 312 attempts, 1,728 edges, length ≈5.243. Both find paths. This observed improvement is not guaranteed: a bigger sample set can change k-nearest neighbors, so edge sets are not necessarily nested and paths need not monotonically improve. A tiny 1-sample, 1-neighbor run can show failure. Probabilistic completeness is asymptotic under assumptions; assert no theorem for this exact fixed-k classroom implementation. PRM* asymptotic optimality is different and outside the timed core. Geometric path success does not validate dynamics, controllers or physical hardware.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
Demo source: demo/demo.py and demo/README.md
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 17
WEEK 04 / CONFIGURATION SPACE & PRM
Live demo: predict, build, animate
Watch one robot pose and one configuration-space point move together.
Robotics & Autonomous Systems · Motion Planning
17
5 min · read the code
12 min · reveal + animate
8 min · compare + recap
Notes: TIMING: 25 minutes. 5 minutes CODE: read robot.py and planner.py. Map forward_points/configuration_free to vertex validity, interpolate/edge_free to local motions, nearest/connect/build_roadmap to construction, query_roadmap to unsampled endpoints and graph copy, shortest_path to Dijkstra. Explicitly show start/goal are added as query vertices rather than snapping to samples. 12 minutes STAGES/PLAYBACK: run python3 week04_motion_planning/demo/demo.py. Preview free start/goal and click (0,0) to display collision. Next stage reveals accepted samples, then checked edges, then search route. Computation was prepared at startup; this is staged disclosure. At final stage Play/Pause animates both panels. Click configuration space to preview and pause; it does not make a new planning query. Resume/replay starts the planned route at its start. Reset returns to first stage/start pose while retaining the roadmap. 8 minutes COMPARISON/CHECKPOINT: run --compare or 20/300 samples with k=10, seed=7. Both documented default cases find a route, denser case shorter here, not a guarantee. Tiny roadmap can fail. Ask what a vertex/edge means, how a new endpoint is attached, whether free endpoints suffice, and what failure means. Playback is kinematic. Saved overview.png and overview_20.png are fallback exports; --export works headlessly. Demo requires Python 3.10+, NumPy, Matplotlib but no ROS/Gazebo. Existing README documents TA-machine validation; our Windows artifact checks are separate. The supplied professor PDF remains referenced but not newly reviewed.
SOURCES
Demo source: demo/demo.py and demo/README.md
Demo source: demo/planner.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 18
OPTIONAL / DEEPER DISCUSSION
Collision geometry
Distance to a link segment becomes capsule clearance.
Robotics & Autonomous Systems · Motion Planning
18
u = clamp(((c−a)·(b−a))/‖b−a‖², 0, 1)
d = ‖c − (a + u(b−a))‖
clearance = min(dlink1, dlink2) − 0.12 − 0.03
Free only when clearance > 0.01 m. Padded contact is blocked.
Notes: TIMING: 0 minutes. Untimed backup. For obstacle center c and segment endpoints a,b, d=b−a. u=clamp(((c−a)·d)/(d·d),0,1); closest point h=a+ud; if d·d=0 use a. Distance=norm(c−h). For both links take minimum distance, subtract physical obstacle radius 0.12 and link capsule radius 0.03 to get clearance. Free iff clearance>.01 padding, equivalently minimum center distance>.16 m. Check contact inclusively as collision. For zero pose link2 lies from (0.6,0) to (1,0), contains obstacle projection (0.8,0), hence center distance 0 and clearance −0.15. Tip at (1,0) lies outside the physical obstacle but the link collides, demonstrating why tip-only checking fails. Physical obstacle outline plus padding is distinct from link radius; do not double-count the radius. Tests place obstacles against each link and test contact; zero-length segment branch should be unit checked separately. Self-collision unmodeled.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py

## Slide 19
OPTIONAL / DEEPER DISCUSSION
Topology and interpolation
The demo uses bounded angles; opposite square edges do not wrap.
Robotics & Autonomous Systems · Motion Planning
19
q₁ (rad)
π
−π
q₂
Boundaries do not wrap.
C = [−π, π] × [−π, π]
q(s) = (1−s)a + sb
Unrestricted revolute joints need a periodic model and metric.
Notes: TIMING: 0 minutes. Untimed backup. Here q belongs to [−π,π]² with hard stops. Though ±π describe equivalent link orientations geometrically, the robot cannot cross that boundary by an infinitesimal wrap; interpolation follows the bounded joint coordinates. From (−3,0) to (3,0) the demo travels through 0 with joint-space length 6 rad. Unrestricted 2R has S1×S1 and shortest circular deltas; it needs an explicitly different metric and interpolation, not just connecting display edges. Full pose wraps are distinct from feasible motion under stops. Formula n=max(1,ceil(max(|Δq1|,|Δq2|)/h)); q_i=a+(i/n)(b−a),i=0..n,h=.01. Resolution is per-coordinate, not necessarily norm increment≤.01; Euclidean step can be √2 × 0.01. Grid display and edge samples serve different purposes; neither is an exact C_obs boundary nor general continuous collision guarantee.
SOURCES
Demo source: demo/robot.py and demo/test_demo.py
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.

## Slide 20
OPTIONAL / DEEPER DISCUSSION
PRM construction and queries
Build once; attach actual endpoints to a query copy.
Robotics & Autonomous Systems · Motion Planning
20
Build roadmap
sample free q choose k neighbors validate local motions store weighted edges
Attach and query
copy roadmap validate + add endpoints check attachments + direct Dijkstra; verify route
Notes: TIMING: 0 minutes. Untimed backup. Construction pseudocode: while accepted<N and attempts<budget draw two uniform angles; accept if free. For each vertex consider k nearest others; deduplicate unordered pairs; retain connect only if edge_free. Store nonnegative length in both adjacency rows. Query: validate free start/goal; copy points and adjacency rows; if equal return [start], 0; append actual endpoints; attach each to k nearest preprocessing vertices with checked edges; consider checked direct edge; Dijkstra; map indices back to configurations. Roadmap metadata records neighbor count, attempts and build time; QueryResult stores path,length,message,query graph. Failure yields [], None, message; invalid inputs ValueError; sampling exhaustion RuntimeError. No mutation of original construction graph, no endpoint snapping. More queries reuse geometry-valid construction only in unchanged scene. The existing GUI supports pose preview, not interactive goal replanning; no new API/demo changes requested.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py

## Slide 21
OPTIONAL / DEEPER DISCUSSION
Dijkstra and useful tests
Small known cases expose mistakes before a large demo.
Robotics & Autonomous Systems · Motion Planning
21
1
1
5
0
1
2
3
isolated
Route [0,1,2], cost 2
Search
Known cost; disconnected; zero length.
Query + geometry
Exact endpoints; copy; blocked midpoint.
Notes: TIMING: 0 minutes. Untimed backup. Exact test graph adjacency: 0 connects 1 with weight 1 and 2 with weight 5; 1 connects 0 and 2 with weight 1; 2 connects 0 with weight 5 and 1 with weight 1; 3 is isolated. Expected shortest 0→2=[0,1,2], cost 2; 0→3=[], None. Test stale-heap handling, cost summation and parent reconstruction. For roadmap geometry check every vertex is free, adjacency symmetry, duplicate/self-exclusion, edge weight equals the norm and checked local motion. Query tests validate exact unsampled endpoint retention, query-copy immutability, disconnected/failed attachment, invalid endpoints, equal endpoints. Sampler deterministic/prefix and finite exhaustion tests; geometry both-link and contact tests; GUI stage/preview/play/pause/reset/arrival tests. Current eight test methods combine these existing checks; some proposed unit checks (nearest ordering, explicit graph storage) are guidance for students rather than claims of existing dedicated test methods. Independently dense path replay reduces risk of shared-predicate bugs. Source review and independent slide checks do not mean existing Python suite ran here; no local Python runtime installed.
SOURCES
Demo source: demo/planner.py and demo/test_demo.py
Demo source: demo/robot.py and demo/test_demo.py

## Slide 22
OPTIONAL / DEEPER DISCUSSION
Sampling and completeness limits
Finite failure, probabilistic completeness, and optimality are different.
Robotics & Autonomous Systems · Motion Planning
22
Finite failure
No route in this graph does not prove no physical route.
Completeness
Asymptotic claims require assumptions.
Optimality
Shortest in this graph is not globally shortest.
No completeness or optimality theorem for this fixed-k demo.
Notes: TIMING: 0 minutes. Untimed backup. Uniform sample probability in a narrow free region is proportional to its measure; a finite sample budget can miss it. Candidate connection choices also matter. A roadmap may be disconnected even though C_free contains a feasible route. Appropriate sampling-based planners have probabilistic completeness results under stated hypotheses as samples grow; no such assertion for every fixed-k variant or this exact code. Completeness concerns finding a path, not least cost. Asymptotic optimality concerns convergence of costs and needs additional algorithms/connection rules, e.g. PRM*, outside this lesson. More accepted samples with the same seed are a point prefix in this demo, but k-neighbor graphs may replace connections and not remain nested. Finite no-route message must not be relabelled impossible. Discuss retrying seed/sample/k choices as possible experiments, not a universal guarantee. Physical applicability needs scene/model/dynamics/control validation beyond geometric sampled collision checking.
SOURCES
https://www.cs.cmu.edu/~motionplanning/papers/sbp_papers/PRM/prmbasic_01.pdf
Retained course reference: MotionPlaningIntroPRM.pdf, credited to Oren Salzman. Introduction 15–20; PRM 4–8, 14, 17, 20–23 (printed slide numbers within sections). Not found locally; not reviewed for this update.